## Slide 1: VPNs & IPsec
Dr. X
Slides adopted by Prof. William Enck, NCSU

## Slide 2: Outline
What is VPN?
IPSec VPN
IPSec VPN vs SSL VPN

## Slide 3: Virtual Private Networks (VPNs)
Provides secure access to private network over public links
  Often, goal is to provide access to corporate network (intranet) from outside (Internet)
  Or, logically join physically separated networks
Achieves some combination of:
  Confidentiality
  Integrity
  Mutual authentication

## Slide 4: Telecommuter VPNs: Client-to-Gateway

## Slide 5: Gateway-to-Gateway VPNs

## Slide 6: How do we build VPNs?
We cannot rebuild the Internet

## Slide 7: VPN Tunneling

## Slide 8: SSL VPN
Which layer?
Layered system:
  the VPN transfers IP packets (of the virtual network) by serializing them on a SSL connection,
  which itself uses TCP as a transport medium,
  which is built over IP packets (on the physical unprotected network).

## Slide 9: IPsec VPN
  IPsec is another technology which is more deeply integrated in the packets
  IPsec VPN more efficient than SSL VPN
  IPsec must be managed quite deep within the operating system network code
  SSL-based VPN only needs some way to hijack incoming and outgoing traffic; the rest can be down in user-level software.

## Slide 10: IPsec
Host level protection service
  IP-layer security (below TCP/UDP)
  De-facto standard for host level security
  Developed by the IETF (over many years)
Available in most operating systems/devices
  E.g., Windows, OS X, Linux, BSD*, ...
Not a single protocol; IPsec is a protocol suite
  Implements a wide range of protocols and cryptographic algorithms
Selectively provides ....
  Confidentiality, integrity, authenticity, replay protection, DoS protection

## Slide 11: IPsec Protocol Suite

## Slide 12: IPsec Architecture

## Slide 13: Internet Key Exchange (IKE)
Two phase protocol used to establish parameters and keys for session
  Phase 1: authenticate peers, establish secure channel via Diffie- Hellman key exchange
  Phase 2: negotiate parameters, establish a security association (SA)
The SA defines algorithms, keys, and policy used to secure the session for a unidirectional traffic flow
  Pairing requires two SAs -- one for each direction
  SAs stored in host’s Security Association Database (SAD)
    Each gateway may define policies for each SA
    Policies stored in the SAD

## Slide 14: IPsec: Packet Handling

## Slide 15: Transport Mode

## Slide 16: Tunnel Mode

## Slide 17: Key Management
Two options:
  Manual: use preshared secrets;or
  Internet Key Exchange (IKE)

## Slide 18: Internet Key Exchange Harkins and Carrel, RFC2409, Nov. 1998
Phase1: KeyExchange (Simplified)
  1. Initiator sends list of supported crypto algos to responder
  2. Responder chooses crypto algo from sender’s list
  3. Initiator sends first half of DH exchange and a nonceI to responder
  4. Responder sends second half of DH exchange, and a nonceR to initiator
  5. Initiator sends its id, its cert, and a sig, all encrypted using key derived from previously exchanged messages
  6. Responder sends its id, its cert, and a sig, all encrypted using key derived from previously exchanged messages

## Slide 19: Internet Key Exchange
Phase II: Security Associations
Using secure channel, establish at least 2 security associations:
  inbound
  outbound

## Slide 20: IPsec and the IP protocol stack
IPsec puts the two main protocols in between IP and the other protocols
  AH: Authentication Header
  ESP: Encapsulating Security Payload
Other functions provided by external protocols and architectures

## Slide 21: Security Association (SA)
An association between a sender and a receiver
  Consists of a set of security related parameters
  E.g., sequence number, encryption key
One way relationship
Determine IPsec processing for senders
Determine IPsec decoding for destination
SAs are not fixed! Generated and customized per traffic flows

## Slide 22: Security Parameter Index (SPI)
A bit string assigned to an SA.
Carried in AH and ESP headers to enable the receiving system to select the SA under which the packet will be processed.
32 bits
  SPI + Dest IP address + IPsec Protocol
Uniquely identifies each SA in SA Database (SAD)

## Slide 23: SA Database (SAD)
Holds parameters for each SA
  Sequence number counter
  Lifetime of this SA
  AH and ESP information
  Tunnel or transport mode
Every host or gateway participating in IPsec has their own SA database

## Slide 24: Authentication Header (AH)
Provides authenticity and integrity
  via HMAC
  over immutable IP headers and data
Advantage: the authenticity of data and IP header information is protected
Disadvantage: the set of immutable IP headers isn’t necessarily fixed
Confidentiality of data is not preserved
Replay protection via AH sequence numbers
  note that this replicates some features of TCP

## Slide 25: IPsec AH Packet Format

## Slide 26: IPsec Authentication
SPI: (spy) identifies the SA for this packet
  Type of crypto checksum, how large it is, and how it is computed
  Really, the policy for the packet
Authentication data
  Hash of packet contents include IP header as specified by SPI
  Treat mutable fields (TTL, header checksum) as zero
  Keyed MD5 Hash is default

## Slide 27: Encapsulating Security Payload
Confidentiality, authenticity, and integrity
  via encryption and HMAC
  over IP payload (data)
Advantage: encapsulated packet is fully secured
Use “null” encryption to get authenticity/integrity only
Note that the TCP/UDP ports are hidden when encrypted
  good: better security, less is known about traffic
  bad: impossible for FW to filter/traffic based on port
Cost: can require many more resources than AH

## Slide 28: ESP Packet Format

## Slide 29: Modes of Operation
Transport: the payload is (optionally) encrypted and the non-mutable fields are integrity verified (via MAC)
Tunnel: each packet is completely encapsulated (and optionally encrypted) in an outer IP packet
  Hides not only data, but some routing information